## Slide 1
SAFETY ORIENTATION
Instructor:
Date:

## Slide 2: SAFETY ORIENTATION
Section 1:
Safety Leadership

## Slide 3: Uncompromising Safety Leaders
Have courage
Are comfortable being out in front while everyone else is behind them
Take a stand when no one else will
Get their energy from transforming and challenging the status quo

## Slide 4: Uncompromising Safety Leaders
Believe that all incidents are preventable
Believe their commitment to safety is non-negotiable
Believe everyone is empowered to be a safety leader
Create the conditions for everyone to safely return home each night

## Slide 5: Uncompromising Safety Leaders
Are familiar with and follow all company and site safety rules
Practice situational awareness
  If they see something at-risk, they address and/or report it immediately
Contribute and participate in toolbox talks and other safety discussions

## Slide 6: SAFETY ORIENTATION
Section 2:
Project-Specific Safety Guidelines

## Slide 7: Grounds for Removal from the Project
Failure to follow policies and procedures
Failure to wear your PPE
Fighting
Alcohol or Drug Use or Possession
Weapons Possession

## Slide 8: Safety Policy and Goals
All incidents are preventable.
Everyone returns home without injury each day.
Everyone is empowered to prevent incidents.
Our goal is to create the conditions to ensure the safety of our employees, subcontractors, customers, and the general public.

## Slide 9: Project-Issued Safety Fines and Violations
Placeholder
Insert your company-specific and/or project-specific safety fines and violations on this slide

## Slide 10: Substance Abuse Policy
We are committed to maintaining a safe and drug-free workplace
We conduct post-incident, random and for cause testing.
For more info, including our Employee Assistance Program (EAP), contact your HR rep
More info can be found at http://www.drugfreeconstruction.org/

## Slide 11: Project-Specific Emergency Action Plan Insert project / company specific info here
Exit Routes
Insert exit route here
Muster Point
Insert muster point here
Medical Information/ Local Hospital
Insert medical info/local hospital info here

## Slide 12: Cell Phone Policy
Cell phone use is prohibited while:
  Conducting job responsibilities
  Operating company vehicles or machinery
  Standing within 10 feet of moving vehicles

## Slide 13: SAFETY ORIENTATION
Section 3:
General Worksite Safety

## Slide 14: Worksite Hazards
OSHA’s Fatal Four:
  Falls
  Electrocution
  Caught in/between objects (trench collapse, pinch points)
  Getting struck by an object (vehicles, falling objects)
Do not enter restricted areas without permission
Ensure work has stopped before entering an area.
Do not work under suspended loads

## Slide 15: Stop Work Authority
Stop Work Authority empowers employees and contract workers with the ability and obligation to stop work if conditions are deemed at-risk
If you see something that doesn’t look right, say something to authorities or your supervisor

## Slide 16: Pre-Job Planning
Also known as:
  Job Safety Analysis (JSA)
  Activity Hazard Analysis (AHA)
  Pre-Task Plan (PTP)
A step by step analysis of a specific activity, the potential hazards associated with the activity and the tools / methods necessary to mitigate those hazards
Consider tasks that will be performed by other trades in proximity to your work

## Slide 17: Globally Harmonized System (GHS)
Ensures information about chemicals, including information and ingredients, can be universally communicated
Formally known as the Hazard Communication Standard (HCS) or Haz-Com

## Slide 18: Safety Data Sheets (SDS)
Provides all information necessary to safely handle a particular chemical
Must be readily accessible to any employee using a hazardous chemical
Any chemical identified with a label that states “Danger, Caution, or Warning” must have a SDS

## Slide 19: Safety Data Sheets (SDS)
Most useful sections to know:
Section 1: Identification
  Chemical name, emergency contact info, recommended use, etc.
Section 2: Hazard(s) Identification
  All hazards regarding the chemical; required label elements
Section 4: First Aid Measures
  Important symptoms/effects, acute, delayed; required treatment
Section 5: Fire-Fighting Measures
  Suitable extinguishing techniques, equipment, chemical hazards from fire

## Slide 20: Safety Data Sheets (SDS)
Section 6: Accidental Release Measures
  Emergency procedures; protective equipment; proper methods of containment and cleanup
Section 7:Handling and Storage
  Precautions for safe handling and storage, including incompatibilities
Section 8: Exposure Controls/Personal Protection
  OSHA’s Permissible Exposure Limits (PELs), ACGIH Threshold Limit Values (TLVs), and any other exposure limit used or recommended by the chemical manufacturer along with personal protective equipment (PPE) requirements

## Slide 21: Housekeeping
Keep your work area clean at all times
Place cords and hoses overhead to prevent tripping hazards
Dispose of trash in the proper containers
Bend or back out nails in scrap lumber

## Slide 22: SAFETY ORIENTATION
Section 4:
Occupational Health
and Wellness

## Slide 23: Silica
Employers must replace crystalline silica materials with safer substitutes whenever possible
When feasible, employers must use engineering or administrative controls such as local exhaust ventilation and blasting cabinets to reduce exposures below the PEL
Use protective equipment or other protective measures if engineering controls are not adequate
Use all available work practices to control dust exposures, such as water sprays and integrated water delivery systems

## Slide 24: Silica
Participate in training, exposure monitoring, health screening, and surveillance programs to monitor any adverse health effects caused by crystalline silica exposures
Be aware of the operations and job tasks that create crystalline silica exposures in your workplace environment and know how to protect yourself
Be aware of the health hazards related to exposures to crystalline silica
Be aware that smoking adds to the lung damage caused by silica exposures

## Slide 25: Silica
Do not eat, drink, smoke, or apply cosmetics in areas where crystalline silica dust is present
  Wash your hands and face outside of dusty areas before performing any of these activities
Wear only a N95 NIOSH certified respirator if respirator protection is required
  Do not alter the respirator
    Do not wear a tight-fitting respirator with a beard or mustache that prevents a good seal between the respirator and the face
Wear disposable or washable work clothes and shower if facilities are available
  Vacuum the dust from your clothes or change into clean clothing before leaving the work site

## Slide 26: Blood Borne Pathogens
If it is reasonably anticipated employees will be exposed to blood or other potentially infectious materials while using first-aid supplies, employers should provide personal protective equipment (PPE) including, but not limited to:
  Gloves
  Gowns
  Face shields
  Masks
  Eye protection

## Slide 27: Injury Reporting
Report all work related injuries to your supervisor immediately
Injury types include, but are not limited to:
  Minor cuts
  Scrapes
  Scratches
  Burns
  Other treatments that require minimal training or technology to administer
Know the location of first aid supplies

## Slide 28: SAFETY ORIENTATION
Section 5:
Personal Protective Equipment

## Slide 29: Head Protection
Wear hard hats where there is a potential for:
  Objects falling from above
  Bumps to the head from fixed objects
  Accidental head contact with electrical hazards
Routinely inspect hard hats for:
  Dents
  Cracks
  Deterioration
Replace after a heavy blow or electrical shock
Maintain in good condition

## Slide 30: Eye Protection
Must be worn onsite at all times
Prescription glasses, with side shields, must meet minimum ANSI requirements

## Slide 31: Hearing Protection
OSHA recommends that workplace noise levels be kept below 90 dBA as an 8-hour time-weighted average
As the noise level increases, it damages your hearing more quickly
If a sound level meter is not available use the 2-to-3 foot rule:
  Stand about an arm’s length away from your coworker
  If you have to raise your voice to be heard 2-3 feet away, assume the sound level is at or above 90 dBA

## Slide 32: Foot Protection
Composite toe footwear is recommended
A minimum 6” boot is highly recommended

## Slide 33: Hand Protection
Insert your company hand protection policy here

## Slide 34: Respiratory Protection
Employers must develop and implement a written respiratory protection program with required work specific procedures
Employers must use NIOSH-certified respirators
Employees must be medically approved and trained before they are assigned a task requiring respirator use
Employees must be fit tested if using a negative or positive pressure tight-fitting facepiece

## Slide 35: High Visibility Clothing
At a minimum, a class II reflective vest should be worn while working onsite
High visibility clothing may be worn in lieu of the vest

## Slide 36: SAFETY ORIENTATION
Section 6:
Fall Protection/
Working at Heights

## Slide 37: Fall Protection
Falls are the #1 cause of injury and death on construction sites
All employees exposed to a fall > 6’, must be effectively tied off
That means the fall distance and anchor point have been calculated / approved by a competent person and is deemed adequate
Harness and lanyards must be inspected daily
Remove from service if defects are found

## Slide 38: Aerial Lifts
Articulating boom lifts
Must be tied off while inside the basket, even if boom is not extended
Must be trained on the specific model that you are operating
Operators must remain in the lift basket at all times (feet on the floor, not railing)
Scissor lifts
Follow manufacturer's, site guidelines for fall protection
Must be trained on the specific model that you are operating
Overhead work warnings (signs, barricades), should be in position

## Slide 39: Guardrail Systems
Typically are 42” in height (+-3”) with a midrail installed at least 21” in height
Must be able to withstand 200 lbs. of force, in any direction, without failure
Top rail deflection must not exceed 3”
Wire rope must be at least ¼” in diameter and flagged every 6’ for visibility

## Slide 40: Personal Fall Arrest Systems (PFAS)
PFAS must be inspected prior to each use for wear, damage, and other deterioration
Defective equipment must not be worn and must be immediately removed from service
Lanyards must be shock absorbing and must be attached to the Dee-ring in the middle of the back at the shoulder level
Anchor points must be able to withstand at least 5,000 lbs.
  Think the weight of a pickup truck

## Slide 41: Personal Fall Arrest Systems (PFAS)
The employer must provide for prompt rescue of employees in the event of a fall
PFAS cannot be attached to guardrail systems
Positioning devices must be rigged so that the employee cannot fall more than 2’
Positioning devices must be connected to an anchor capable of supporting at least twice the load impact or 3,000 lbs., whichever is greater

## Slide 42: SAFETY ORIENTATION
Section 7:
Fire Safety

## Slide 43: Fire Protection
Fire extinguishers must be conspicuously located and periodically inspected
Travel distance to an extinguisher must not exceed 100’
In a multistory building, extinguishers must be located at each stairwell on every level
A fire extinguisher must be within 50’ of any outdoor storage of flammable liquids exceeding 5 gallons

## Slide 44: Flammable Liquids
Flammable liquids must be stored in metal safety cans containing a spring loaded top and a flash arrestor
Flammable liquids must not be stored near stairwells or other access / egress points
Flammable liquids may not be stored in plastic containers
No more than 25 gallons of flammable liquids may be stored in a room outside of an approved storage cabinet
Outdoor storage must not exceed 1,100 gallons, in any one area, and be positioned at least 20’ from any building

## Slide 45: Liquefied Petroleum (LP-Gas)
LP-Gas containers must not be stored within buildings, regardless of whether they are full or empty
When stored outdoors, containers must be in a suitable, well ventilated enclosure
At least one 20-BC fire extinguisher must be in place
Outdoor storage distance from buildings is as follows:
  < 500 lbs 0’
  501-6,000 lbs 10’
  6,001-10,000 lbs 20’
  > 10,000 lbs 25’

## Slide 46: SAFETY ORIENTATION
Section 8:
Equipment and Tools

## Slide 47: Heavy Equipment
Do not operate vehicles in reverse with an obstructed rear view unless it has a reverse signal alarm capable of being heard above ambient noise levels or a signal observer indicates that it is safe to move
Be aware of blind spots
Make eye contact with the operator when entering their work area
Only use equipment for its intended purpose
Maintain a minimum 10’ safe working distance from electric lines

## Slide 48: Ladders and Stairways
A ladder or stair must be provided at all work points of access where the break in elevation is > 19” and no ramp, runway, sloped embankment, or personnel hoist is provided
A double cleated ladder or two or more separate ladders must be in position when there are 25 or more employees in an elevated work area

## Slide 49: Ladders
Maintain a 3-point contact
  Two hands and a foot, or two feet and a hand when climbing/ descending a ladder
Stay near the middle of the ladder and face the ladder while climbing up or down
Only put ladders on a stable and level surface that is not slippery
Extend the top of the ladder three feet above the landing

## Slide 50: Ladders
Stepladders must be opened fully and locked while in use
  They cannot be used as straight ladders
Ladders must be secured to prevent accidental displacement
Ladders must be used as designed
  Not as scaffold planks, “bridges”, etc.
Set the ladder at the proper angle
  When a ladder is leaned against a wall, the bottom of the ladder should be one-quarter of the ladder’s working length away from the wall

## Slide 51: Scaffolds
Each scaffold and scaffold component must support– without failure– its own weight and at least 4 times the maximum intended load applied or transmitted to it
A qualified person must design the scaffolds, which are loaded in accordance with that design
Each platform must be planked and decked as fully as possible with the space between the platform and uprights not more than 1 inch
Scaffold planking must be able to support, without failure, its own weight and at least four times the intended load

## Slide 52: Scaffolds
Supported scaffolds are platforms supported by legs, outrigger beams, brackets, poles, frames, or similar rigid support
The structural members must be plumb and braced to prevent swaying and displacement
  Poles, legs, posts, frames, and uprights
Supported scaffolds with a height to base width ratio of more than 4:1 must be restrained by guying, tying, bracing, or an equivalent means
Supported scaffolds' poles, legs, posts, frames, and uprights must bear on base plates and mud sills, or other adequate firm foundation

## Slide 53: Scaffolds
Guardrails or PFAS must be used when the fall hazard exceeds 6’
Scaffolds must be inspected by a competent person before each shift and should be tagged that it’s safe to access
Scaffolds must not be moved while employees are working from them
Cross braces cannot be used for access / egress

## Slide 54: Cranes
Ground conditions
  The controlling entity must ensure that ground conditions are safe for the crane to be assembled and used
  The Assembly / Disassembly (A /D) director determines if safe ground conditions are present
Cranes must remain a minimum of 10’ from overhead high voltage (OHHV) lines
The employer must assume the OHHV lines are energized unless the utility confirms that they are not
A competent person must inspect the crane prior to each shift

## Slide 55: Cranes
Operators must be certified by one of four entities:
  An accredited crane operator certification testing organization
  An audited employer program
  Qualification by the U.S military
  Licensing by a government entity
Swing radius must be barricaded to prevent accidental contact
The employer must ensure that each signal person meets the standard’s qualification requirements

## Slide 56: Hoisting and Lifting
Only certified riggers are allowed to control loads
Tag lines must be used to control loads
Alterations and modifications may not be made to any material or personnel hoists unless approved by the manufacturer
Signal persons must be qualified by the employer
Only on person may signal a crane at a time

## Slide 57: Hand and Power Tools
Power tools must be fitted with guards and safety switches
When replacing grinding wheels, make sure the RPM rating on the wheel exceeds the motor rating
Exposed moving parts of power tools need to be safeguarded including, but not limited to:
  Belts, gears, shafts, pulleys, sprockets, spindles, drums, flywheels, chains, or other reciprocating, rotating, or moving parts

## Slide 58: Hand and Power Tools
To protect user from shock and burns:
  Electric tools must have a three-wire cord with a ground
  Must be plugged into a grounded receptacle, be double insulated, or be powered by a low-voltage isolation transformer
  Third prong must never be removed from the plug
When using pneumatic tools:
  A safety clip or retainer must be installed to prevent attachments such as chisels on a chipping hammer from being ejected during tool operation

## Slide 59: Hand and Power Tools
If an air hose is more than 1/2-inch in diameter:
  A safety excess flow valve must be installed at the source of the air supply to reduce pressure in case of hose failure
  Pneumatic power tools must be secured to the hose with a whip-check device to prevent accidental disconnection
Powder-actuated tools operate like a loaded gun and must be treated with extreme caution
Proof of training must be with the operator at all times

## Slide 60: Materials Handing
Back Injury Prevention
  Have materials delivered as close to where they will be used as possible
  Use pallet jacks and hand trucks to transport heavy items
  Ask for help if lifting heavy objects
  Maintain neutral and straight spine alignment whenever possible

## Slide 61: Materials Handling
Proper Lifting Procedure
  Kneel on one knee and pull load onto knee before standing
  Bending at the knees, not the waist, helps maintain proper spine alignment
  Place materials that are to be manually lifted at "power zone" height, about mid-thigh to mid-chest
  Turn your whole body, not just your waist, when lifting or lowering materials
  Move items close to your body and use your legs when lifting an item from a low location

## Slide 62: Welding and Cutting
Valve protection caps shall be in place and secured when transporting, moving, and storing compressed gas cylinders
Compressed gas cylinders shall be secured in an upright position at all times
Oxygen cylinders in storage shall be separated from fuel-gas cylinders or combustible materials, a minimum distance of 20 feet or by a noncombustible barrier at least 5 feet high having a fire-resistance rating of at least one-half hour
Torches shall be lighted by friction lighters or other approved devices, and not by matches or from hot work

## Slide 63: Welding and Cutting
Cylinders shall be kept far enough away from the actual welding or cutting operation so that sparks, hot slag, or flame will not reach them; when this is impractical, fire resistant shields shall be provided
No welding, cutting, or heating shall be done where the application of flammable paints, or the presence of other flammable compounds, or heavy dust concentrations creates a hazard
Suitable fire extinguishing equipment shall be immediately available in the work area and shall be maintained in a state of readiness for instant use

## Slide 64: SAFETY ORIENTATION
Section 9:
Working Over or Near Water

## Slide 65: Working Over or Near Water
Employees working over or near water, where the danger of drowning exists, shall be provided with U.S. Coast Guard-approved life jacket or buoyant work vests
Ring buoys with at least 90 feet of line shall be provided and readily available for emergency rescue operations. Distance between ring buoys shall not exceed 200 feet
At least one lifesaving skiff shall be immediately available at locations where employees are working over or adjacent to water
Landscapers, and other employees working on slopes adjacent to water, should take additional precautions

## Slide 66: SAFETY ORIENTATION
Section 10:
Electrical Safety

## Slide 67: Electrical Safety
Look for overhead power lines and buried power line indicators
Stay at least 10 feet away from overhead power lines and assume they are energized
Use factory-assembled cord sets and only extension cords that are 3-wire type
Use only cords, connection devices, and fittings that are equipped with strain relief
Use ground-fault circuit interrupters (GFCIs) on all 120-volt, single-phase, 15- and 20-ampere receptacles, or have an assured equipment grounding conductor program (AEGCP)

## Slide 68: Electrical Safety
Extension and power cords shall be protected from sharp edges and potential pinch points
Temporary lights must be protected by cage guards
Extension cords must have a strain relief device to prevent excessive pull from being transmitted to the terminal screws
Electrical tape cannot be used to repair nicks in extension and power cords
Circuits must be locked and tagged out prior to employees working on them

## Slide 69: SAFETY ORIENTATION
Section 11:
Motor Vehicles and Maintenance of Traffic

## Slide 70: Motor Vehicles and Mechanized Equipment
All vehicles and equipment must be checked at the beginning of each shift to ensure that all parts and accessories that affect the safe operation are free from defects
Any vehicle or equipment, with an obstructed view to the rear, must have a back up alarm or a spotter in place while backing
Heavy machinery or equipment beds must be blocked against falling or pinching hazards while employees are working under them

## Slide 71: Traffic Control and Flagging
All traffic control must be performed in accordance with the Manual of Uniform Traffic Control Devices (MUTCD) along with state and local guidelines
Flaggers must use the STOP / SLOW paddle when flagging, not an orange / red flag

## Slide 72: SAFETY ORIENTATION
Section 12:
Excavation and Trenching

## Slide 73: Excavations and Trenching
Specific excavation requirements:
  Contact “Miss Utility” at 811 to locate underground utilities prior to excavating
  Employees working in an excavation >5’ in depth must be protected by a sloping or shoring system
  Soil must be classified by a competent person using at least one manual and visual test
  Excavations must be inspected daily by a competent person
  Shoring systems must extend at least 2’ above the surrounding surface so as the prevent material or debris from entering the excavation

## Slide 74: SAFETY ORIENTATION
Section 13:
Permits

## Slide 75: Hot Work Permit
Insert company policy here

## Slide 76: Confined Space Entry
Confined spaces have three criteria:
  Large enough for a worker to enter
  Limited means of entry or exit
  Not designed for continuous occupancy
Before workers can enter a confined space, employers must provide pre-entry planning, including:
  Having a competent person evaluate the work site for the presence of confined spaces, including permit-required confined spaces

## Slide 77: Confined Space Entry
Once the space is classified as a permit required confined space, identify:
  The means of entry and exit
  Proper ventilation methods
  Elimination or control of all potential hazards in the space

## Slide 78: Work Permit
Add specific company policy here

## Slide 79: SAFETY ORIENTATION
Section 14:
Concrete and Masonry Construction

## Slide 80: Concrete and Masonry Construction
No employee shall be allowed to work under concrete buckets
To the extent practical, elevated concrete buckets shall be routed so no employee, or the fewest number of employees, are exposed
Concrete troweling machines must be equipped with a “dead man” switch
Protruding rebar, onto which employees could fall, must be protected against impalement hazards

## Slide 81: Concrete and Masonry Construction
A limited access zone (LAZ) shall be established whenever a masonry wall is being built
The zone shall be equal to the height of the finished wall plus 4’
All masonry walls > 8’ must be braced to prevent collapse
Masonry saws must be guarded with a semicircular guard over the blade

## Slide 82: SAFETY ORIENTATION
Section 15:
Steel Erection

## Slide 83: Steel Erection
General requirements:
  Each employee engaged in steel erection on an unprotected deck > 15’ must be protected by PFAS, guardrail or safety net systems
  Connectors working more than 2 stories or 30’, whichever is less, must be protected by PFAS, guardrail or safety net systems
  Best practice: employees must be protected at 6’
  Shear connectors cannot be installed until after metal decking is placed

## Slide 84: Steel Erection
  Columns must be anchored with at least 4 anchor bolts, structural members must have at least 2 bolts
  Controlled decking zones (CDZ) must be clearly marked and used only by employees in leading edge work
  Many companies require a 6’ fall protection requirement rule, regardless of the type of work performed

## Slide 85: SAFETY ORIENTATION
Conclusion and
Final Questions

## Slide 86: Conclusion
Safety is everyone’s responsibility!
If you see something, say something
You can contribute to saving 800 lives per year

## Slide 87: Thank you!
Please contact (insert instructor name and contact information) for further information